Clock cycle and Analysis regarding
BRISCV

---
Duration of 1 clock cycle
- Always #1 clock = ~clock;
- Toggle clock every 1 time units
- 1 clock cycle = 2 ns

---
Clock requirements for 1 ALU instruction hit in I-cache: 00500093 ( addi x1, x0, 5)
- Alu instruction gets hit in I cache, shown in Instr_hit0 line
- No memory accesss
- Time taken = (148 – 144) ns = 4 ns = 2 clock cycles
- After each instruction, Nop instruction get execute by default
- Register write is happening in the second clock cycle

---
Execution of 3 consecutive Alu instructions

---
Timing analysis of load hit(I-cache+D-cache) instruction : 0b402083 (lw x1, 180(x0))
- No dealy for I-cache or D-cache miss
- Clock cycles consumed = (280 - 274) ns = 6ns = 3 clock cycles
- Data_hit0 becomes 1 after 1 clcok cycle from the begin of the execution of this instruction

---
Timing analysis of store hit(I-cache+D-cache) instruction : 0a202823( sw x1, 176(x0))
- No dealy for I-cache or D-cache miss
- Clock cycles consumed = (284 - 280) ns = 4ns = 2 clock cycles
- Data_hit0 becomes 1 after 1 clcok cycle from the begin of the execution of this instruction
- As no write back stage in store location, required one clock cycle less than load hit.

---
Time required to execute 1 miss Instruction cycle : NOP(00000013)
- Instruction miss occurs
- Time taken to fetch from memory to cache and then execute = (144-2)ns = 142 ns

---
State changes during I-cache miss
Reset
Reset
Idle
Cache
Access
Wait
For
access
Cache
Access
wait
Read
state
Update

---
Clock cycle calculation
From the above diagram we can calculate the following parameters:
- Clock cycle in case of instruction miss + fetch + execute = 144ns – 2ns = 142ns
- Clock cycle for a hit instruction (no memory access) = 2ns + 2ns = 4 ns, as compulsory NOP instruction is executed after each instruction, provided by the processor.
- Instr_hit0 signal line initially was low,
- After fetching 4 instructions in I-cache, Instr_hit0 toggles and remain high for consecutive 3 instructions, as shown in the above diagram.

---
load_test.dat : instructions

---
Following parameters can be calculated
- First instruction is the load instruction, total clock cycle needed = 276 ns
- I-cache miss occurs
- From 142 ns instr_hit0 line becomes high
- D-cache miss occurs
- It takes (276-142)ns = 134 ns
- From 268 ns tag value got changed to exclusive state

---
store_test.dat : instructions

---
Following parameters can be calculated
- First instruction is the store instruction, total clock cycle needed = 144 ns
- I-cache miss occurs
- From 142 ns instr_hit0 line becomes high
- From 144ns to 274 ns next instruction executes
- Next instruction takes (274-144)ns = 130 ns
- It is an Alu opearation(register-register) instruction, only need 4 ns
- From 268 ns tag value got changed to modified state

---
My Findings
- Instr_hit0, was initially 0, then switches to 1 for hit instructions
- Data are brought to memory in case of store miss also
- In case of load miss, PC is incrementing to 4, only after completing the load opeartion including I-miss and D-miss
- In case of store miss, PC is incrementing to 4, only after finishing I-cache miss issue, while resolving D-cache miss issue, fetching data from memory, PC points to the next instruction, which elongates the execution of next instruction.

---
D-cache changed after store operation

---
After load operation

---
Memory written back